## Slide 1: GLA UNIVERSITY
Computer Network

## Slide 2: Outline
Introduction Concepts:
  Goals and Applications of networks
  Network structure and architecture
  The OSI reference model and services
  Network topology design
  Physical Layer Transmission Media
  Line coding scheme
  Switching methods (circuit switching, Packet switching)
  TDM

## Slide 3: Introduction Concepts

## Slide 4: Introduction
Network
It is defined as a medium which is responsible for carrying the
data from one node to another
Eg: intranet, internet, PAN, etc

## Slide 5: Introduction
Computer Network
A computer network is comprised of nodes and links
A node is the end point whereas links are the medium
It is defined as a network through which one system can communicate with the other system

## Slide 6: Goals of network
The main goals of network are:
Resource sharing
  Eg: printer on network, shared drives, etc
High reliability
  Eg: alternative sources, multiple copies, etc
Increase system utilization
  Eg: load sharing, pooling, etc
Powerful communication medium
  Eg: update is reflected immediately

## Slide 7: Application of network
The main applications of network are:
Accessing web
File transfer
File sharing
Remote procedure call, etc

## Slide 8: Network architecture
Network architecture is the design of a computer network
It is a framework for the specification of a network's physical
components and their functional organization
It also defines the set of rules which are followed during
communication (also known as protocols)
Network architecture refers to the way network devices and services are structured to serve the connectivity needs of client devices
A architecture defines how the computers should get connected to get the maximum advantages of a computer network such as better response time, security, scalability, etc

## Slide 9: Network architecture
The two most common network architecture are
Peer-to-Peer
  Known as P2P
Client-Server
  Known as tiered

## Slide 10: P2P architecture
All the nodes in a network are inter-connected with every other nodes
There is no one who acts as a master (also known as server) for all,
rather all acts as a master independently
It is useful for small environment

## Slide 11: P2P architecture
Advantages
Less costly as there is no central server
In case of a node failure, other nodes in the network are not affected
Installation is quite easy
Disadvantages
Each computer has to take the backup of its own
Security measures are to be
nodes
taken by all the independently
Scalability is a issue

## Slide 12: Client-Server architecture
All the nodes in a network are connected with the central node (known as master/server)
The master node receive request from all the other nodes (clients) and respond their request

## Slide 13: Client-Server architecture
Advantages
Data backup is easy
Performance is
better as the
is greatly
response time improves
Security is better as unauthorized access are denied by server
Scalability is not an issue in this architecture as large number of computers can be connected with server.
Disadvantages
In case of server failure, the
entire network is down.
Server maintenance cost is high
Cost is high

## Slide 14: Network topology
The topology defines how the nodes in the network are connected
It also defines the flow of data from one node to another
There are five types of topologies defines
  Mesh topology
  Star topology
  Bus topology
  Ring topology
  Hybrid topology

## Slide 15: Network topology
Mesh topology
In this topology, each node is connected to every other node in the network
Implementing the mesh topology is expensive and difficult
In this type of topology, each node may send message to destination through multiple paths
While the data is travelling, it is automatically configured to reach the destination by taking the shortest route which means the least number of hops

## Slide 16: Network topology
Star topology
Each node is connected to a central device called a hub
The hub takes a request from any node and pass it to the other node
Data on a star topology passes through the hub, switch, or
concentrator before continuing to its destination
The hub, switch, or concentrator manages and controls all functions of the network
The star topology reduces the chance of network failure by connecting all of the systems to a central node

## Slide 17: Network topology
Bus topology
All the nodes topology are connected by one single cable
A bus topology consists of a main run of cable with a terminator at each end. All nodes (file server, workstations, and peripherals) are connected to the linear cable
Popular on LANs because they are inexpensive and easy to install

## Slide 18: Network topology
Ring topology
In a ring topology, every device has exactly two neighbors for
communication purposes.
All messages travel through a ring in the same direction.
A failure in any cable or node breaks the loop and can take down the
entire network
To implement a ring network we use the Token Ring technology
A token, or small data packet, is continuously passed around the network. When a device needs to transmit, it reserves the token for the next trip around, then attaches its data packet to it

## Slide 19: Network topology
Hybrid topology
A combination of any two or more network topologies
A hybrid topology always accrues when two different basic network topologies are connected
It is a mixture of above mentioned topologies. Usually, a central computer is attached with sub-controllers which in turn participate in a variety of topologies

## Slide 20: Network Technologies
It can be classified under two category
Based on transmission technology
Based on scale

## Slide 21: Network Technologies
Based on transmission technology
Broadcast
  Broadcast network have a single communication channel that is shared by all the nodes on the network
Point to point
  There may exist multiple paths between a source-destination pair and the nodes in between provide a route to move the data from one to other until it reach to the destination

## Slide 22: Network Technologies
Based on scale
Local Area Network (LAN)
Metropolitan Area Network (MAN)
Wide Area Network (WAN)

## Slide 23: Network Technologies
Based on scale
LAN
  usually privately owned
  used to links the devices in a single office, building or campus of up to few
distance
  restricted in size
  run at speeds of 10 to 100 Mbps (but now much higher speeds can be
achieved)
  most common topologies are bus, ring and star

## Slide 24: Network Technologies
Based on scale
MAN
  designed to extend over the entire city
  may be a single network or a connection of number of LANs

## Slide 25: Network Technologies
Based on scale
WAN
  provides long-distance transmission of data over large geographical areas that may comprise a country, continent or even the globe
  not restricted in size

## Slide 26: What is a network?
Every network includes:
At least two nodes
A cable or wireless pathway, called Transmission Media
Rules, called Protocols, so that computers can use the unified principle of data communication
Networking Interface Cards (NIC)

## Slide 27: Why Layered Architecture?
To make the design process easy by breaking unmanageable tasks into several smaller and manageable tasks (by divide-and-conquer approach)
Modularity and clear interfaces, so as to provide comparability between the different providers' components
Ensure independence of layers, so that implementation of each layer can be changed or modified without affecting other layers
Each layer can be analyzed and tested independently of all other layers

## Slide 28: OSI reference model
OSI stands for Open Systems Interconnection
It has been developed by ISO – “International Organization of
Standardization”
It is a 7 layer architecture
Each layer is responsible for specific functionality
All these 7 layers work collaboratively to transmit the data from one end (top to bottom) and receive the data at other end (bottom to top)

## Slide 29: OSI reference model (terminology)
Protocol
– is a formal set of rules and conventions that governs how computers
exchange information over a network medium.

## Slide 30: OSI reference model
Application Layer
Presentation Layer Session Layer Transport Layer Network Layer Data link Layer Physical Layer

## Slide 31: OSI reference model and its services
Application Layer
This layer is responsible to generate the data, which has to be transferred over the network
Eg: browser

## Slide 32: OSI reference model and its services
Presentation Layer
The data from the application layer is extracted here and converted as per the required format to transmit over the network
The functions of the presentation layer
are :
  Translation
  Encryption/ Decryption
  Compression

## Slide 33: OSI reference model and its services
This layer is responsible for establishment of connection, maintenance of sessions, authentication and security
Session Layer

## Slide 34: OSI reference model and its services
Transport Layer
The data in the transport layer is referred to as
segments
It is responsible for the End to End delivery of the complete message
The transport
acknowledgement
layer also provides the of the successful data
transmission and re-transmits the data if an error is found
Two type of services are provided:
  Connection oriented
  Connection less

## Slide 35: OSI reference model and its services
Network layer works for the transmission of data
It also takes care of packet routing i.e. selection of the shortest path
The sender & receiver’s IP address are
placed in the header by the network layer.
Network Layer

## Slide 36: OSI reference model and its services
Data link Layer
The main function of this layer is to make sure data transfer is error-free from one node to another, over the physical layer
When a packet arrives, it is the
responsibility of DLL to transmit it to the
Host using its MAC address.
Data Link Layer is divided into two sub layers :
Logical Link Control (LLC)
Media Access Control (MAC)

## Slide 37: OSI reference model and its services
Physical Layer
It is responsible for the actual physical connection between the devices
The physical layer contains information in the form of bits
It is responsible for transmitting
individual bits
When receiving data, this layer will get the signal and convert it into 0s and 1s and send them to the Data Link layer, which will put the frame back together.

## Slide 38: OSI reference model and its services (in brief)
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data link Layer
Physical Layer
Provides service to the user
Performs translation, compression and encryption
Manage session
Responsible for end- to-end transmission of data
Data into packets and putting network header
Packets into frames, error free transfer and mapping
Frames into bits and a
medium of transfer

## Slide 39: OSI reference model and its services (review)
Application Layer
DATA
DATA
To: Presentation layer
From: Presentation layer
Sender
Receiver

## Slide 40: OSI reference model and its services (review)
responsible for generating the data
contains a variety of protocols that
are commonly needed by users
  HTTP
  FTP
  SMTP
Application Layer

## Slide 41: OSI reference model and its services (review)
Application Layer
Presentation Layer
Encode, Encrypt,
Compress
Decode, Decrypt,
Decompress
To: Session layer
From: Session layer
Sender Receiver
From: Application layer
To: Application layer

## Slide 42: OSI reference model and its services (review)
Purpose
– Make
different data representations
it possible for computers with
to
communicate
Concerns
  Syntax and semantics of information transmitted
  Understands the nature of the data being transmitted
  Converts ASCII, EBCDIC, etc
Application Layer
Presentation Layer

## Slide 43: OSI reference model and its services (review)
Session Layer
Sync and recovery
Sync and recovery
To: Transport layer
From: Transport layer
Sender Receiver
From: Presentation layer
To: Presentation layer

## Slide 44: OSI reference model and its services (review)
Purpose
  Allow users on different machines to
establish sessions between them
Concerns
  Authentication and authorization
  Check Pointing
  Dialog control
  Logical grouping of operation
  Synchronization
Application Layer
Presentation Layer
Session Layer

## Slide 45: OSI reference model and its services (review)
Application Layer
Presentation Layer
Session Layer
Transport Layer
Break data into
segments
Merge segments to
form data
To: Network layer
From: Network layer
Sender Receiver
From: Session layer
To: Session layer
DATA |  |  |  | 
DS1 | DS2 | DS3 | … | DSn

## Slide 46: OSI reference model and its services (review)
Transport Layer
Break data into
segments
Merge segments to
form data
To: Network layer
From: Network layer
Sender Receiver
From: Session layer
To: Session layer
Two protocols used in this layer:
TCP – follow same route
UDP – may follow same route

## Slide 47: OSI reference model and its services (review)
Transport Layer
Break data into
segments
Merge segments to
form data
To: Network layer
From: Network layer
Sender Receiver
From: Session layer
To: Session layer
Function of this layer:
Service point addressing
Segmentation and reassembling
Connection control
Flow control
Error control

## Slide 48: OSI reference model and its services (review)
Service Decisions: What type of service to provide; error-free point to point, datagram, etc
End-to-end: it carries data all the way from the source
to the destination
Reliability: Ensures that packets arrive at their destination
Hides network: Allows details of the network to be
hidden from higher level layers
Mapping: Determines which messages belong to which connection
Flow control: keeps a fast transmitter from flooding a slow receiver
Application Layer • Purpose
– Accept data from above it, split it up into smaller
Presentation Layer units, pass them to network layer, and ensure that the
pieces all arrive correctly at the other end
Concerns
Session Layer
Transport Layer

## Slide 49: OSI reference model and its services (review)
Network Layer
Break segments into
packets
Merge packets to
form segments
To: DLL
From: DLL
Sender Receiver
From: Transport layer
To: Transport layer
DS1 |  |  |  | 
DSP1 | DSP2 | DSP3 | … | DSPn
Protocol used:
IP

## Slide 50: OSI reference model and its services (review)
Purpose
– Route packets from source to destination
Concerns
Routing: What path is followed by packets from source to destination. Can be based on a static table, can be determined when the connection is created, or can be highly dynamic, being determined a new for each packet, to reflect the current network load
Congestion: Controls the number packets in the subnet
QoS: Quality of Service provided
Fragmentation
Heterogeneity: Interfacing so that one type of network can talk to another
Addressing, packet size, protocols
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer

## Slide 51: OSI reference model and its services (review)
Data link Layer
Break packets into
frames
Merge frames to
form packets
To: Physical layer
From: Physical layer
Sender Receiver
From: Network layer
To: Network layer
DSP1 |  |  |  | 
DSPF1 | DSPF2 | DSPF3 | … | DSPFn

## Slide 52: OSI reference model and its services (review)
Data link Layer
It contains two sub-layers:
Logical Link Control Layer
  It identifies the address of the network layer protocol from the header
  It also provides flow control
Media Access Control Layer
  A Media access control layer is a link between the Logical Link Control layer and the network's physical layer

## Slide 53: OSI reference model and its services (review)
Purpose
– Transform a raw transmission line into a line that appears free of undetected transmission errors to the networks layer
Concerns
Framing: Breaks apart input data into frames
and transmit the frames sequentially
Error handling: if the service is reliable, the receiver confirms correct receipt of each frame by sending back an acknowledgement frame
Flow control: keeps a fast transmitter from drowning a slow receiver in data
Physical Addressing
Access Control (CSMA/CD, Token passing)
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data link Layer

## Slide 54: OSI reference model and its services (review)
Break frame into
bits
Merge bits to form
frame
Sender Receiver
From: DLL
To: DLL
medium
Physical Layer
DSPF1 |  |  |  | 
1 | 1 | 0 | … | 1

## Slide 55: OSI reference model and its services (review)
Purpose
  Transmits raw bits across a medium
Functional
  Flow of data (simplex, half duplex, full
duplex)
  Topology
  Encoding
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data link Layer
Physical Layer

## Slide 56: An exchange using OSI reference model
A A
P P
S S
T T
N N
D D
P P
medium
data
data
data
data
data
data
data
data
data
data
data
data
data
data
56

## Slide 57: TCP/IP reference model
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Data link Layer
Physical Layer
Application Layer
Transport Layer
Internet Layer
Link Layer

## Slide 58: TCP/IP reference model

## Slide 59: TCP/IP reference model
Concepts central to the OSI model
  Services
  Interfaces
  Protocols
OSI has good definition of service, interface, and protocol. Fits well with object oriented programming concepts.
Protocols are better hidden
TCP/IP model did not distinguish between service, interface, and protocol
With TCP/IP, the protocols came first; model was just a description of the protocols

## Slide 60: Transmission Mode
Three types of data flow mode can be used
  Simplex
  Half duplex
  Full duplex

## Slide 61: Transmission Mode
Simplex
  there is only unidirectional flow of data
  only one of the node on a link can transmit, the other can only receive
  this mode use the entire capacity of the channel to send data in one direction
  Eg: one way road

## Slide 62: Transmission Mode
Half duplex
  there is bidirectional flow of data but at a time only one node can send
  each node can both transmit and receive, but not at the same time
  when one node is sending, the other can only receive, and vice versa
  the entire capacity of the channel can be utilized for each direction
  Eg: walkie-talkies

## Slide 63: Transmission Mode
Full duplex
  there is bidirectional flow of data
  each node can both transmit as well as receive simultaneously which can be achieved by two ways
    either the link must contain two physically separate transmission paths, one for
sending and other for receiving OR
    the capacity is divided between signals travelling in both directions
  the entire capacity of the channel can be utilized for both direction
  Eg: mobile communication

## Slide 64: Networking Hardware
Networking hardware includes all computers, peripherals, interface cards and other equipment needed to perform data- processing and communications within the network like
  Network Interface Card
  Switch
  Router
  Bridge etc

## Slide 65: Networking Hardware
Network Interface Card
  Network interface cards, commonly referred to as NICs, are used to connect
a PC to a network
  The NIC provides a physical connection between the networking cable and
the computer's internal bus
  NICs come in three basic varieties: 8-bit, 16-bit, and 32-bit. The larger the number of bits that can be transferred to the NIC, the faster the NIC can transfer data to the network cable

## Slide 66: Networking Hardware
Network Interface Card

## Slide 67: Networking Hardware
Hub
  A hub joins multiple computers (or other network devices) together to form
a single network
  On this network, all computers can communicate directly with each other
  The networking hub is a junction box with several ports in the back for receiving the Ethernet cables that are plugged into each computer on the LAN

## Slide 68: Networking Hardware
Hub (Types)
  Passive: This type of hub does not amplify or boost the signal. It does not manipulate or view the traffic that crosses it. The passive hub does not require electrical power to work.
  Active: It amplifies the incoming signal before passing it to the other ports. It requires AC power to do the task.
  Intelligent: They are also called as smart hubs. It function as an active hub and also include diagnostic capabilities. They also provide flexible data rates to network devices. It also enables an administrator to monitor the traffic passing through the hub and to configure each port in the hub.

## Slide 69: Networking Hardware
Repeater
  Since a signal loses strength as it passes along a cable, it is often necessary
to boost the signal with a device called a repeater
  A repeater is an electronic device that receives a signal, cleans the unnecessary noise, regenerates it, and retransmits it at a higher power level so that the signal can cover longer distances without degradation

## Slide 70: Networking Hardware
Switch
  A network switch is a small hardware device that joins multiple computers
together within one network
  Network switches appear nearly identical to network hubs, but a switch
generally contains more intelligence than a hub
  Unlike hubs, network switches are capable of inspecting data packets as they are received, determining the source and destination device of each packet, and forwarding them appropriately
  Allow several users to send information over a network at the same time without slowing each other down

## Slide 71: Networking Hardware
Router
  A device to interconnect SIMILAR networks, e.g. similar protocols and
workstations and servers
  A router is an electronic device that interconnects two or more computer
networks, and selectively interchanges packets of data between them
  Each data packet contains address information that a router can use to determine if the source and destination are on the same network, or if the data packet must be transferred from one network to another

## Slide 72: Networking Hardware
Bridge
  A bridge is a device that connects a local network to another local network
  The function of a bridge is to connect separate networks together
  Bridges map the Ethernet addresses of the nodes residing on each network segment and allow only necessary traffic to pass through the bridge. When a packet is received by the bridge, the bridge determines the destination and source segments

## Slide 73: Networking Hardware
Bridge (types)
  Local bridges: Directly connect local area networks (LANs)
  Remote bridges: Can be used to create a wide area network (WAN) link between LANs
  Wireless bridges: Can be used to join LANs or connect remote stations to
LANs (wirelessly)

## Slide 74: Networking Hardware
Gateway
  Gateways are used to interconnect two different networks having different
protocols
  Networks using different protocols use different addressing formats
  A gateway is a network point acts as an entrance to another network
  Gateways are also called protocol converters

## Slide 75: Difference
Bridge:
  device to interconnect two LANs that use the SAME logical link control
protocol but may use different medium access control protocols
Router:
  device to interconnect SIMILAR networks, e.g. similar protocols and
workstations and servers
Gateway:
  device to interconnect DISSIMILAR protocols and servers

## Slide 76: Difference
Hub
Physical layer
signal or bits
Non-intelligent device
LAN
Half duplex
MAC address
Switch
Data link layer
frames
Intelligent device
LAN
Half/Full duplex
MAC address
MAN,
Network layer
packets
Intelligent device
LAN, WAN
Full duplex
IP address
Router

## Slide 77: Addressing

## Slide 78: Addressing
Four levels of addresses are used in an internet employing the TCP/IP protocols:
  physical address,
  logical address,
  port address, and
  application-specific address.
Each address is related to a one layer in the TCP/IP architecture

## Slide 79: Addressing
Application Layer
Transport Layer Internet Layer Link Layer
Application specific
Port address Logical address
Physical address

## Slide 80: Addressing
Eg:
87 10 Data
1
packet accepted
87 10 Data
4

## Slide 81: Addressing
local area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon
Eg:
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address

## Slide 82: Addressing
The physical addresses will change from hop to hop, but the logical addresses may remain the same.

## Slide 83: Addressing
A port address is a 16-bit integer address represented by one decimal number
This number is assigned automatically by the OS, manually by the user or is set as a default for some popular applications.
Eg:
753, 443, 8080, etc
A 16-bit port address represented as one single decimal number

## Slide 84: Addressing
Notable well-known port numbers
• | 20 | File Transfer Protocol (FTP) Data Transfer
• | 21 | File Transfer Protocol (FTP) Command Control
• | 22 | Secure Shell (SSH) Secure Login
• | 25 | Simple Mail Transfer Protocol (SMTP) E-mail routing
• | 53 | Domain Name System (DNS) service
• | 67, 68 | Dynamic Host Configuration Protocol (DHCP)
• | 80 | Hypertext Transfer Protocol (HTTP)
• | 110 | Post Office Protocol (POP3)
• | 161 | Simple Network Management Protocol (SNMP)
• | 443 | HTTP Secure (HTTPS) HTTP over TLS/SSL

## Slide 85: Analog and Digital data
Data can be analog or digital
Analog data is continuous and takes continuous values
Digital data have discrete states and takes discrete values

## Slide 86: Data and Signals

## Slide 87: Analog and Digital signal
Signals can be analog or digital
Analog signals can have an infinite number of values in a range
Digital signals can have only a limited number of values

## Slide 88: Difference
Analog
Analog signals are difficult to get
analyzed at first
Analog signals are more accurate
Analog signals take time to be
stored
Analog signals produce too much noise
Eg: Human voice, Thermometer,
Analog phones etc
Digital
Digital signals are easy to
analyze
Digital signals are less accurate
Digital signals can be easily
stored
Digital signals do not produce noise
Eg: Computers, Digital Phones,
Digital pens, etc

## Slide 89: Periodic and Non-periodic
A periodic signal completes a pattern within a measurable time frame, called a period, and repeats that pattern. The completion of one full pattern is called a cycle.
A non periodic signal changes without exhibiting a pattern or cycle that repeats over time

## Slide 90: Periodic and Non-periodic
Period refer to amount of time in second a signal need to complete 1 cycle
Frequency refer to number of period in 1 s
They are the inverse of each other

## Slide 91: Periodic and Non-periodic
Value
• • •
Time
The sine wave is the most fundamental form of a periodic analog signal

## Slide 92: Periodic and Non-periodic
Peak amplitude

## Slide 93: Signal

## Slide 94: Units of period and frequency

## Slide 95
Eg
Express a period of 100 ms in microseconds.

## Slide 96
Solution
The equivalents of 1ms (1 ms is 10–3 s) and 1s (1s is 106 μs) By substituting:
100 ms
= 100 * 10-3 s
= 100 * 10-3 * 106 μs
= 105 μs

## Slide 97: The power we use at home has a frequency of 60 Hz. What is the period of that wave?
Solution
T = 1/f
= 1/60 s
= 0.0166 s
= 0.0166 * 103 ms
= 16.6 ms
Eg

## Slide 98: The period of a signal is 100 ms. What is its frequency in kilohertz?.
Eg
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10–3 kHz).

## Slide 99: Frequency
Frequency is the rate of change with respect to time
Change in a short span of time means high frequency
Change over a long span of time means low frequency
  If a signal does not change at all, its frequency is zero
  If a signal changes instantaneously, its frequency is infinite

## Slide 100: Phase
The term PHASE, or PHASE SHIFT, describes the position of the waveform relative to time 0
A complete cycle is defined as 360 degrees of phase
Phase difference , also called phase angle , in degrees is conventionally
defined as a number greater than -180, and less than or equal to +180
Leading phase refers to a wave that occurs "ahead" of another wave of the same frequency. Lagging phase refers to a wave that occurs "behind" another wave of the same frequency.

## Slide 101: Phase
Eg:
– A sine wave is offset 1/6 cycle with respect to time 0. What is its phase in
degrees and radians?
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is
1/6 * 360
= 60°
= 60 * 2Π/360 rad
= Π/3 rad

## Slide 102: Application of Simple Signals
Simple sine waves have many applications in daily life
We can send a single sine wave to carry electric energy from one
place to another
  Eg: electric power
  an alarm to a security center

## Slide 103: Signals and Communication
A single-frequency sine wave is not useful in data communications
We need to send a composite signal, a signal made of many simple
sine waves
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases

## Slide 104: Composite Signals and Periodicity
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies
If the composite signal is non-periodic, the decomposition gives a combination of sine waves with continuous frequencies

## Slide 105: Composite Period Signal
A Composite Signal is collection of multiple single simple signals

## Slide 106: Decomposition of a composite periodic signal
Amplitude
f
3f 9f
b. Frequency-domain decomposition of the composite signal
Frequency
Amplitude
• • •
Time

## Slide 107: Decomposition of a composite non-periodic signal

## Slide 108: Bandwidth
The range of frequencies contained in a composite signal is its bandwidth
The bandwidth is normally a difference between two numbers
Eg:
– if a composite signal contains frequencies between 1000 and 5000, its bandwidth is 5000 − 1000, or 4000

## Slide 109: Bandwidth

## Slide 110: Bandwidth

## Slide 111: Bandwidth
Eg:
– If a periodic signal is decomposed into five sine waves with frequencies of
100, 300, 500, 700, and 900 Hz, what is its bandwidth?
Solution
Let fh be the highest frequency, fl the lowest frequency, and BW
the bandwidth. Then,
BW = fh – fl
= 900 – 100
= 800 Hz

## Slide 112: Bandwidth
Eg:
– A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz.
What is the lowest frequency?
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the
bandwidth. Then,
B = fh – fl
20 = 60 – fl
fl = 40 Hz

## Slide 113: Bandwidth
Eg:
– A non-periodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz

## Slide 114: Fourier Analysis
Fourier analysis is a tool that changes a time domain signal to a frequency domain signal and vice versa
Time domain ↔ frequency domain

## Slide 115: Digital Signals
In addition to being represented by an analog signal, information can also be represented by a digital signal
Eg:
– 1 can be encoded as a positive voltage and a 0 as zero voltage
A digital signal can have more than two levels

## Slide 116: Digital Signal

## Slide 117: Digital Signal

## Slide 118: Digital Signal
Eg:
– A digital signal has eight levels. How many bits are needed per level?
Solution
number of levels = 2n
8 = 2n
log28 = log22n log28 = n log22 n = 3

## Slide 119: Digital Signal
Eg:
– A digital signal has nine levels. How many bits are needed per level?

## Slide 120: Bit Rate
The term Bit Rate is used to describe digital signals
The bit rate is the number of bits sent in 1s, expressed in bits per
second (bps).

## Slide 121: Transmission Impairment
Signals travel through transmission media, which are not perfect, the imperfection causes signal impairment (damage/loss/weak)
This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium. What is sent is not what is received
Three causes of impairment are attenuation, distortion, and noise
Impairment causes
Distortion
Attenuation
Noise

## Slide 122: Impairment

## Slide 123: Impairment
Attenuation and Amplification

## Slide 124: Impairment
Attenuation and Amplification
Eg:
– Suppose a signal travels through a transmission medium and its power is reduced to one half. This means that P2 = 0.5 P1. In this case, the attenuation (loss of power) can be calculated as
Solution
10 log10 P2/P1
= 10 log10 (0.5 P1/P1)
= 10 log10 (0.5)
= 10 (-0.3)
= -3 dB

## Slide 125: Impairment
Attenuation and Amplification
Eg:
– A signal travels through an amplifier, and its power is increased 10 times. This means that P2 = 10P1. In this case, the amplification (gain of power) can be calculated as
Solution
10 log10 P2/P1
= 10 log10 (10 P1/P1)
= 10 log10 (10)
= 10 (1)
= 10 dB

## Slide 126: Impairment
Attenuation and Amplification
Eg:
– How much total gain/loss in signal from point 1 to point 4
Solution

## Slide 127: Impairment
Attenuation and Amplification
Eg:
– Sometimes the decibel is used to measure signal power in milliwatts. In this case, it is referred to as dBm and is calculated as dBm = 10 log10 Pm, where Pm is the power in milliwatts. Calculate the power of a signal if its dBm =
−30
Solution
10 log10 Pm = dBm 10 log10 Pm = -30 log10 Pm = -3
Pm = 10-3 mW

## Slide 128: Impairment
Attenuation and Amplification
Eg:
– The loss in a cable is usually defined in decibels per kilometer (dB/km). If the signal at the beginning of a cable with −0.3 dB/km has a power of 2 mW, what is the power of the signal at 5 km?
Solution
Loss in the cable is (-0.3) * 5 = -1.5 dB Now, the power can be calculated as 10 log10 P2/P1 = -1.5
log10 P2/P1 = -0.15
P2/P1 = 10-0.15 = 0.7
P2 = 0.7P1
P2 = 0.7*2 = 1.4 mW

## Slide 129: Impairment
Distortion
Distortion means that the signal changes its form or shape
Distortion can occur in a composite signal made of different frequencies
Each signal component has its own propagation speed through a medium and, therefore, its own delay in arriving at the final destination
Differences in delay may create a difference in phase if the delay is not exactly the same as the period duration

## Slide 130: Impairment
Distortion

## Slide 131: Impairment
Noise
Noise is another cause of impairment
Several types of noise, such as thermal noise, induced noise, crosstalk, etc may corrupt the signal
  Thermal noise is the random motion of electrons in a wire, which creates an extra signal not originally sent by the transmitter
  Induced noise comes from sources such as motors
  Crosstalk is the effect of one wire on the other
Noise is measured in terms of SNR ( Signal to Noise Ratio)

## Slide 132: Impairment
Noise

## Slide 133: Two cases of SNR: a high SNR and a low SNR

## Slide 134: How to Calculate SNR

## Slide 135: SNR
Eg:
– The power of a signal is 10 mW and the power of the noise is 1 μW. What
are the values of SNR and SNRdB?
Solution
The values of SNR and SNRdB can be calculated as follows:
SNR = 10 * 10-3/10-6
= 10 * 103
= 10000 dB SNRdB = 10 log1010000
= 10 log10104
= 40 dB

## Slide 136: SNR
The values of SNR and SNRdB for a noiseless channel are Solution
SNR = (signal power)/0
= ∞
SNRdB = 10 log10 ∞
= ∞
We can never achieve this ratio in real life; it is an ideal

## Slide 137: Noiseless Channel: Nyquist Rate

## Slide 138: Nyquist Rate
Eg:
– Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a
signal with two signal levels. The maximum bit rate can be calculated as
Solution
Bit rate = 2 * 3000 * log22
= 6000 bps

## Slide 139: Nyquist Rate
Eg:
– Consider the same noiseless channel transmitting a signal with 2 bits for
each level. The maximum bit rate can be calculated as
Solution
Bit rate = 2 * 3000 * log24
= 12000 bps

## Slide 140: Noisy Channel: Shannon Capacity

## Slide 141: Noisy Channel: Shannon Capacity
Eg:
– Consider an extremely noisy channel in which the value of the signal-to-
noise ratio is almost zero. For this channel the capacity C is calculated as
Solution
C = BW * log2(1 + SNR)
= BW * log2(1+0)
= BW * 0
= 0
This means that the capacity of this channel is zero regardless of the bandwidth. In other words, we cannot receive any data through this channel

## Slide 142: Noisy Channel: Shannon Capacity
Eg:
– Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The
theoretical channel capacity can be calculated as
Solution
dB 10
SNR = 10 log SNR
36 = 10 log10SNR
SNR = 103.6
SNR = 3981
C = BW * log2(1+SNR)
= 2 * 106 * log23982
= 2 * 106 * 11.95
= 24 Mbps

## Slide 143: Noisy Channel: Shannon Capacity
Eg:
  We have a channel with a 1-MHz bandwidth. The SNR for this channel is
63. What are the appropriate bit rate and signal level?
Solution
  First, we use the Shannon formula to find the upper limit
  Then we use the Nyquist formula to find the number of signal levels
C = BW * log2(1+SNR)
= 106 * log264
= 6 Mbps
Bit rate = 2 * BW * log2L
2
6 = 2 * 1 * log L
L = 23 = 8

## Slide 144: Latency or Delay

## Slide 145: Types of delay
Propagation speed
  speed at which a bit travels though the medium from source to destination
Transmission speed
  the speed at which all the bits in a message arrive at the destination
(difference in arrival time of first and last bit)

## Slide 146: Types of delay
Queuing delay
  is the time spent by the packet in a queue, waiting to be transmitted onto the
link
Processing delay
  time taken by the routers to process the packet header

## Slide 147: Bandwidth
One characteristic that measures network performance is bandwidth
However, the term can be used in two different contexts with two different measuring values
  bandwidth in hertz
  bandwidth in bits per second

## Slide 148: Bandwidth
The first, bandwidth in hertz, refers to the range of frequencies in a composite signal or the range of frequencies that a channel can pass
The second, bandwidth in bits per second, refers to the speed of bit transmission in a channel or link, often referred to as Capacity

## Slide 149: Throughput
The throughput is a measure of how fast we can actually send data through a network
OR
How much data can be transferred from source to destination in a given time frame
A link may have a bandwidth of BW bps, but we can only send T bps through this link with T always less than B (T < B)

## Slide 150: Bandwidth-Delay
Bandwidth and delay are two performance metrics of a link

## Slide 151: Bandwidth-Delay
Sender
After 5 s
Receiver
1st bit |  |  |  | 
2nd bit | 1st bit |  |  | 
3rd bit | 2nd bit | 1st bit |  | 
4th bit | 3rd bit | 2nd bit | 1st bit | 
5th bit | 4th bit | 3rd bit | 2nd bit | 1st bit
After 1 s
After 2 s
After 3 s
After 4 s

## Slide 152: Bandwidth-Delay
Sender
Receiver
After 5 s
After 1 s
After 2 s
After 3 s
After 4 s

## Slide 153: Delay
151
Eg:
– A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
Throughput = (12000 * 10000)/60
= 2 * 106
= 2 Mbps

## Slide 154: Delay
Eg:
– What is the propagation time if the distance between the two points is
12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable
Solution
We can calculate the propagation time as
Propagation Time = (12000 * 1000)/(2.4 * 108)
= 0.05 s
= 50 ms

## Slide 155: Delay
Eg:
– What are the propagation time and the transmission time for a 2.5 KB message if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s
Solution
Propagation Time = (12000 * 1000)/(2.4 * 108)
= 0.05 s
= 50 ms
Transmission Time = (2.5 * 103 * 8)/(109)
= 20000/109
= 0.00002 s = 0.02 ms

## Slide 156: Delay
Eg:
– What are the propagation time and the transmission time for a 5 MB message if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s
Solution
Propagation Time = (12000 * 1000)/(2.4 * 108)
= 50 ms
Transmission Time = (5 * 106 * 8)/(106)
= 40 s